## Slide 1: Active-Routing: Compute on the Way for Near-Data Processing
Jiayi Huang, Ramprakash Reddy Puli, Pritam Majumder Sungkeun Kim, Rahul Boyapati, Ki Hwan Yum and EJ Kim

## Slide 2: Outline
Motivation
Active-Routing Architecture
Implementation
Enhancements in Active-Routing
Evaluation
Conclusion

## Slide 3: Motivation

## Slide 4: Data Is Exploding
Graph processing (social networks)
Deep learning (NLP) [Hestess et al. 2017]
…
………
Requires more memory to process big data
Ref: https://griffsgraphs.files.wordpress.com/2012/07/facebook-network.png

## Slide 5: Demand More Memory
DRAM layer
3D die-stacked memory [Loh ISCA’08]
  HMC and HBM
  Denser capacity
  higher throughput
Memory network [Kim et al. PACT’13]
  Scalable memory capacity
  Better processor bandwidth
Vault Controller
Intra-Cube Network
I/O
I/O
I/O
I/O
… …
Vault Controller
Logic Layer
Vault

## Slide 6: Enormous Data Movement Is Expensive
Stall processor computation
Consume energy
Processing-in-memory (PIM)
  PIM-Enabled Instruction (PEI) [Ahn et al. ISCA’2015]
  C = A x B (Can we bring less data?)
In-network computing
  Compute in router switches [Panda IPPS’95, Chen et al. SC’11]
  MAERI [Kwon et al. ASPLOS’18]
Near-data processing to reduce data movement
Active-Routing for dataflow execution in memory network
Active-Routing for dataflow execution in memory network
Reduce data movement and more flexible
Active-Routing for dataflow execution in memory network
Reduce data movement and more flexible
Exploit memory throughput and network concurrency

## Slide 7: Active-Routing Architecture

## Slide 8: System Architecture
Host CPU
Host CPU
Network-on-Chip
O3core
Cache
O3core
Cache
…
HMC Controller
HMC
Network
Interface
Network
Interface
…
Memory Network

## Slide 9: Active-Routing Flow
Active-Routing tree dataflow for compute kernel
Compute kernel example
  Reduction over intermediate
  results
Active-Routing tree dataflow
for (i = 0; i < n; i++) {
sum += *Ai × *Bi;
}
Host CPU
Ai
Bi

## Slide 10: Active-Routing Three-Phase Processing
Active-Routing Tree Construction
Host CPU
Ai
Bi
for (i = 0; i < n; i++) {
sum += *Ai × *Bi;
}
Update Packet

## Slide 11: Active-Routing Three-Phase Processing
Active-Routing Tree Construction
Update Phase for data processing
Host CPU
Ai
Bi
for (i = 0; i < n; i++) {
sum += *Ai × *Bi;
}
Ak Operand request
Bk Operand request
Ak Operand response
Bk Operand response

## Slide 12: Active-Routing Three-Phase Processing
Active-Routing Tree Construction
Update Phase for data processing
Gather Phase for tree reduction
Host CPU
Ai
Bi
for (i = 0; i < n; i++) {
sum += *Ai × *Bi;
}
Gather request
Gather request
Gather request
Gather request
Gather request
Gather request

## Slide 13: Implementation

## Slide 14: Programming interface and ISA extension
Update(void *src1, void *src2, void *target, int op);
Gather(void *target, int num_threads);
API
Extended PIM Instructions
Active-Routing Execution
for (i = 0; i < n; i++) {
sum += *Ai × *Bi;
}
for (i = 0; i < n; i++)
{
Update(Ai, Bi, &sum, MAC);
}
Gather(&sum, 16);

## Slide 15: Programming interface and ISA extension
Update(void *src1, void *src2, void *target, int op);
Gather(void *target, int num_threads);
Offloading logic in network interface
  Dedicated registers for offloading information
  Convert to Update/Gather packets
API
Extended PIM Instructions
Active-Routing Execution

## Slide 16: Active-Routing Engine
Vault Controller
Intra-Cube Network
I/O
I/O
I/O
I/O
… …
Vault Controller
Logic Layer
DRAM layer
Vault
Vault Controller
Intra-Cube Network
I/O
I/O
I/O
I/O
…
Vault Controller
Active-Routing Engine
Logic Layer
Packet Processing Unit
Flow Table
Operand Buffers
ALU

## Slide 17: Packet Processing Unit
Process Update/Gather packets
Schedule corresponding actions
Packet Processing Unit
Flow Table
Operand Buffers
ALU

## Slide 18: Flow Table
Flow Table Entry
Packet Processing Unit
Flow Table
Operand Buffers
ALU
64-bit | 6-bit | 64-bit | 64-bit | 64-bit | 2-bit | 4-bit | 1-bit
flowID | opcode | result | req_counter | resp_counter | parent | children flags | Gflag

## Slide 19: Flow Table
Flow Table Entry
Packet Processing Unit
Flow Table
Operand Buffers
ALU
64-bit | 6-bit | 64-bit | 64-bit | 64-bit | 2-bit | 4-bit | 1-bit
flowID | opcode | result | req_counter | resp_counter | parent | children flags | Gflag

## Slide 20: Flow Table
Flow Table Entry
  Maintain tree structure
Packet Processing Unit
Flow Table
Operand Buffers
ALU
64-bit | 6-bit | 64-bit | 64-bit | 64-bit | 2-bit | 4-bit | 1-bit
flowID | opcode | result | req_counter | resp_counter | parent | children flags | Gflag

## Slide 21: Flow Table
Flow Table Entry
  Maintain tree structure
  Keep track of state information of each flow
Packet Processing Unit
Flow Table
Operand Buffers
ALU
64-bit | 6-bit | 64-bit | 64-bit | 64-bit | 2-bit | 4-bit | 1-bit
flowID | opcode | result | req_counter | resp_counter | parent | children flags | Gflag

## Slide 22: Flow Table
Flow Table Entry
  Maintain tree structure
  Keep track of state information of each flow
Packet Processing Unit
Flow Table
Operand Buffers
ALU
64-bit | 6-bit | 64-bit | 64-bit | 64-bit | 2-bit | 4-bit | 1-bit
flowID | opcode | result | req_counter | resp_counter | parent | children flags | Gflag

## Slide 23: Operand Buffers
Operand Buffer Entry
Packet Processing Unit
Flow Table
Operand Buffers
ALU
64-bit | 64-bit | 1-bit | 64-bit | 1-bit
flowID | op_value1 | op_ready1 | op_value2 | op_ready2

## Slide 24: Operand Buffers
Operand Buffer Entry
  Shared temporal storage
Packet Processing Unit
Flow Table
Operand Buffers
ALU
64-bit | 64-bit | 1-bit | 64-bit | 1-bit
flowID | op_value1 | op_ready1 | op_value2 | op_ready2

## Slide 25: Operand Buffers
Operand Buffer Entry
  Shared temporal storage
  Fire for computation in dataflow
Packet Processing Unit
Flow Table
Operand Buffers
ALU
64-bit | 64-bit | 1-bit | 64-bit | 1-bit
flowID | op_value1 | op_ready1 | op_value2 | op_ready2
More details in our paper

## Slide 26: Enhancements in Active-Routing

## Slide 27: Multiple Trees Per Flow
Single tree from one memory port
  Deep tree
  Congestion at memory port
Host CPU
Deep tree
Congestion

## Slide 28: Multiple Trees Per Flow
Build multiple trees
  ART-tid: interleave the thread ID
  ART-addr: nearest port based on operands’ address
Host CPU
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 29: Exploit Memory Access Locality
Pure reduction
  Irregular (random)
  Regular
Reduction on intermediate results
  Irregular-Irregular (II)
  Regular-Irregular (RI)
  Regular-Regular (RR)
Offload cache block granularity for regular accesses
for (i = 0; i < n; i++) {
sum += *Ai;
}
for (i = 0; i < n; i++) {
sum += *Ai × *Bi;
}

## Slide 30: Evaluation

## Slide 31: Methodology
Compared techniques
  HMC Baseline
  PIM-Enabled Instruction (PEI)
  Active-Routing-threadID (ART-tid)
  Active-Routing-address (ART-addr)
Tools: Pin, McSimA+ and CasHMC
System configurations
  16 O3 cores at 2 GHz
  16 memory cubes in dragonfly topology
  Minimum routing with virtual cut-through
  Active-Routing Engine
  1250 MHz, 16 flow table entries, 128 operand entries

## Slide 32: Workloads
Benchmarks (graph app, ML kernels, etc.)
  backprop
  lud
  pagerank
  sgemm
  spmv
Microbenchmarks
  reduce (sum reduction)
  rand_reduce
  mac (multipy-and-accumulate)
  rand_mac

## Slide 33: Comparison of Enhancements in Active-Routing
Chart: Normalized Speedup over HMC Baseline
| backprop | lud | pagerank | sgemm | spmv | gmean
ART-Naïve | -0.79363 | -0.18598 | 0.091128 | -1.2477 | -0.32846 | -0.49292
ART-tid
ART-addr

## Slide 34: Comparison of Enhancements in Active-Routing
Chart: Normalized Speedup over HMC Baseline
| backprop | lud | pagerank | sgemm | spmv | gmean
ART-Naïve | -0.79363 | -0.18598 | 0.091128 | -1.2477 | -0.32846 | -0.49292
ART-tid | 0.10909 | 0.62686 | 0.1239 | 1.2325 | -0.057038 | 0.40707
ART-addr

## Slide 35: Comparison of Enhancements in Active-Routing
Chart: Normalized Speedup over HMC Baseline
| backprop | lud | pagerank | sgemm | spmv | gmean
ART-Naïve | -0.79363 | -0.18598 | 0.091128 | -1.2477 | -0.32846 | -0.49292
ART-tid | 0.10909 | 0.62686 | 0.1239 | 1.2325 | -0.057038 | 0.40707
ART-addr | 0.10947 | 0.6243 | 0.12613 | 1.4762 | 0.41194 | 0.5496
Multiple trees and cache-block grained offloading effectively make ART much better.

## Slide 36: Benchmark Performance
Chart: Normalized Runtime Speedup
| backprop | lud | pagerank | sgemm | spmv | gmean
PEI | 1 | 1 | 1 | 1 | 1 | 1
ART-tid
ART-addr

## Slide 37: Benchmark Performance
Chart: Normalized Runtime Speedup
| backprop | lud | pagerank | sgemm | spmv | gmean
PEI | 1 | 1 | 1 | 1 | 1 | 1
ART-tid | 1.0934 | 0.87896 | 1.3747 | 4.2347 | 0.3616 | 1.1513
ART-addr

## Slide 38: Benchmark Performance
Chart: Normalized Runtime Speedup
| backprop | lud | pagerank | sgemm | spmv | gmean
PEI | 1 | 1 | 1 | 1 | 1 | 1
ART-tid | 1.0934 | 0.87896 | 1.3747 | 4.2347 | 0.3616 | 1.1513
ART-addr | 1.0943 | 0.87379 | 1.3818 | 7.421 | 1.0646 | 1.5986
In general, ART-addr > ART-tid > PEI
Imbalance computations

## Slide 39: Analysis of spmv

## Slide 40: Benchmark Performance
Chart: Normalized Runtime Speedup
| backprop | lud | pagerank | sgemm | spmv | gmean
PEI | 1 | 1 | 1 | 1 | 1 | 1
ART-tid | 1.0934 | 0.87896 | 1.3747 | 4.2347 | 0.3616 | 1.1513
ART-addr | 1.0943 | 0.87379 | 1.3818 | 7.421 | 1.0646 | 1.5986
PEI cache thrashing
C = A x B

## Slide 41: Microbenchmark Performance
Chart: Normalized Runtime Speedup
| reduce | rand_reduce | mac | rand_mac | gmean
PEI | 1 | 1 | 1 | 1 | 1
ART-tid | 25.4126 | 8.3179 | 4.6937 | 2.1243 | 6.7756
ART-addr | 52.5927 | 15.9836 | 6.2817 | 2.8444 | 11.0705
ART-addr > ART-tid > PEI

## Slide 42: Energy-Delay Product
Chart: Normalized Energy-Delay-Product (log)
| backprop | lud | pagerank | sgemm | spmv | gmean
ART-tid | -0.08929 | 0.091138 | -0.074366 | -1.698 | 0.45251 | -0.26361
ART-addr | -0.089687 | 0.047433 | -0.072198 | -1.9399 | -0.10473 | -0.43182
Reduce EDP by 80% on average

## Slide 43: Dynamic Offloading Case Study (lud)
ART-tid-adaptive: dynamic offloading based on locality and reuse
Chart: Phase
Chart: Speedup
| ART-tid | ART-tid-adaptive
 | 1 | 2.2979
First Phase
Second Phase

## Slide 44: Conclusion
Propose Active-Routing in-network computing architecture which computes near-data in the memory network in data-flow style
Present a three-phase processing procedure for Active-Routing
Categorize memory access patterns to exploit the locality and offload computations in various granularities
Active-Routing achieves up to 7x speedup with 60% average performance improvement and reduce energy-delay product by 80% on average

## Slide 45: Thank You & Questions
Jiayi Huang
jyhuang@cse.tamu.edu

## Slide 46: Active-Routing: Compute on the Way for Near-Data Processing
Jiayi Huang, Ramprakash Reddy Puli, Pritam Majumder Sungkeun Kim, Rahul Boyapati, Ki Hwan Yum and EJ Kim